## Slide 1: Analog Signal Conditioning Using LTspice
Name: Melvin Dileep Cyriac
Student ID: 125EI0015
Selected Op-Amp: AD8051

## Slide 2: Project Objective
Design a non-inverting amplifier (Gain = 10).
1
Design an RC low-pass filter with cutoff frequency ≈ 1 kHz.
2
Integrate amplifier and filter into a complete signal chain.
3
Verify the design using LTspice transient and AC simulations.
4

## Slide 3: Why AD8051?
Gain-Bandwidth Product: 110 MHz.
Slew Rate: 145 V/µs.
High-speed commercial operational amplifier.
Real SPICE model available for LTspice.

## Slide 4: Design Calculations
Amplifier Gain: Av = 1 + R2/R1
Selected values: R1 = 10 kΩ, R2 = 90 kΩ.
Av = 1 + 90k/10k
Low-pass filter: fc = 1/(2πRC)
Selected values: R = 10 kΩ, C = 15.9 nF --> fc = 1 kHz.

## Slide 5: Simulation Results (SIM-2)
Input: 100 mV at 100 Hz (0.1fc).
Amplifier output ≈ 1 V peak.
RC filter caused negligible attenuation.
The purpose of this simulation was to check if the amplifier and filter work correctly at a low frequency, which is 100 Hz. Our filter was designed with a cutoff frequency of 1 kHz

## Slide 6: Simulation Results (SIM-5)
Passband gain ≈ 20 dB. (20log10​(10)=20 dB)
Cutoff frequency ≈ 1 kHz.
Gain decreases above cutoff frequency.
SIM-5 is an AC sweep of the complete signal chain. Instead of testing one frequency, LTspice automatically tests many frequencies from 10 Hz to 100 kHz and shows how the circuit responds.
Green line- This is the output of the amplifier before the RC filter. Because the amplifier has a gain of 10. 20log10​(10)=20 dB
Blue line- This is the output after the RC low-pass filter. At low frequencies, it is almost the same as the amplifier output. As the frequency increases, it starts getting smaller.

## Slide 7: Sim 5 graph

## Slide 8: Results Summary
Theoretical gain = 10; Simulation ≈ 10.
The RC filter (R = 10 kΩ, C = 15.9 nF) was designed with a cutoff frequency of about 1 kHz. Signals below 1 kHz passed through almost unchanged, while signals above 1 kHz became weaker. This shows that the filter successfully removes high-frequency noise while allowing the useful low-frequency signal to pass.
The non-inverting amplifier successfully achieved the designed voltage gain of 10 (+20 dB) using R1 = 10 kΩ and R2 = 90 kΩ. Both theoretical calculations and LTspice simulations showed an output of approximately 1 V from a 100 mV input, confirming the amplifier design.
Passband gain ≈ 20 dB.
Filter cutoff ≈ 1 kHz.
Real AD8051 shows finite bandwidth unlike the ideal op-amp.

## Slide 9: Conclusion
Successfully designed and simulated an analog signal conditioning chain.
Theoretical calculations agreed closely with LTspice results.
Compared ideal and real op-amp behaviour.
Learned amplifier design, RC filtering and AC analysis.